## Slide 1: Universal Mechanism
Predicting wear of railway wheel profiles in program package
"Universal Mechanism": methods and approaches

## Slide 2: Contents
Parallel discrete approach to wear modeling
Wheel/rail contact models for wear simulation
Wear models
Profile-updating procedure
UM Loco/Wheel Profile Wear Evolution tool
Example

## Slide 3: The parallel discrete approach to wear modeling
1
The "Parallel" means that different configurations of rail vehicles are modeled in parallel, with the same wheel profiles for all configurations. Configurations differ in track macrogeometry, track irregularities, vehicle mass and so on. The set of configurations should be a representative set of conditions in which the rail vehicle is operated.
The "Discrete" means that the track length traveled by the vehicle during the simulation is divided into a sequence of intervals (wear steps). The number of intervals is the same for all configurations. Within each interval the profiles are not changed. At the end of each wear step, a wear depth is scaled according to a mileage assigned to one wear step. After scaling, the wear depth is summarized for the respective wheels by taking into account the weight (statistical) factors of the configurations and the wear symmetry, if any. Then the profiles are updated according to accumulated wear depth.

## Slide 4: The parallel discrete approach to wear modeling
2
Scheme of wear simulation
n
1
2
3
n – number of wear steps

## Slide 5: Contents
Parallel discrete approach to wear modeling
Wheel/rail contact models for wear simulation
Wear models
Profile-updating procedure
UM Loco/Wheel Profile Wear Evolution tool
Example

## Slide 6: Wheel/rail contact models for wear simulation
3
Contact model by W. Kik and J. Piotrowski + FASTSIM algorithm;
CONTACT library.
Example of a multi-point non-Hertzian wheel/rail contact

## Slide 7: Contents
Parallel discrete approach to wear modeling
Wheel/rail contact models for wear simulation
Wear models
Profile-updating procedure
UM Loco/Wheel Profile Wear Evolution tool
Example

## Slide 8: Wear models
4
Archard model
where is the volume wear [m3];
is the wear coefficient [m3/J];
is the work of frictional forces [J].
where is the power of frictional forces [W].
where is the tangential traction [Pa];
is the sliding velocity [m/s];
is the contact patch area [m2].
While using the FASTSIM-like algorithms, the work of frictional forces is calculated according to the following formula:
where is the wheelset velocity [m/s];
is the integration time step size [s]
is the creep [-].
x
y

## Slide 9: Wear models
5
Specht model
where is the critical power density of frictional forces [W/m2];
is the jump coefficient [-].
A [J/ mm2]
mild wear regime
W [μg/ mm2]
severe wear regime

## Slide 10: Contents
Parallel discrete approach to wear modeling
Wheel/rail contact models for wear simulation
Wear models
Profile-updating procedure
UM Loco/Wheel Profile Wear Evolution tool
Example

## Slide 11: Profile-updating procedure
6
Wear mask
before wear step
Histogram of distribution of volume wear
after wear step
wear step
1
Accumulation of volume wear for every separate wheel of a wheelset

## Slide 12: Profile-updating procedure
7
2
Taking into account the symmetry of wear
Symmetrical wear of wheel profiles of same wheelset
where , is the volume wear for the left and the right wheels of the wheelset calculated for the configuration at motion with speed .
Symmetrical wear of wheelsets
where is the number of wheelsets.
3
Scaling volume wear according to a mileage assigned to one wear step
4
Sum of volume wear for every wheel
where is the weight of configuration;
is the weight of speed;
is the number of configurations.

## Slide 13: Profile-updating procedure
8
5
Calculation of wear depth in the center of each circumferential strip
where is the smoothed volume wear;
is the arc-coordinate of the center of the strip ;
is the wheel radius;
is the width of wear accumulation interval.
6
Profile updating
where is the external normal for the wheel profile.

## Slide 14: Contents
Parallel discrete approach to wear modeling
Wheel/rail contact models for wear simulation
Wear models
Profile-updating procedure
UM Loco/Wheel Profile Wear Evolution tool
Example

## Slide 15: UM Loco/Wheel Profile Wear Evolution tool
9

## Slide 16: Contents
Parallel discrete approach to wear modeling
Wheel/rail contact models for wear simulation
Wear models
Profile-updating procedure
UM Loco/Wheel Profile Wear Evolution tool
Example

## Slide 17: Example
10
Freight car with 23t axle-load
No. | Macrogeometry | Weight | V [km/h] | Weights
1 | Tangent | 0.8 | 40 | 0.294
 |  |  | 60 | 0.540
 |  |  | 80 | 0.166
2 | Curve R = 650 m | 0.15 | 40 | 0.294
 |  |  | 60 | 0.540
 |  |  | 80 | 0.166
3 | Curve R = 350 m | 0.05 | 50 | 1
Set of configurations
*Synthetic track irregularities correspond to a track of a good quality
GOST 10791-2011 wheel profile
R65 rail profile
Worn R65 rail profile

## Slide 18: Example
Flange wear
Tread wear
Wheel profile in new state and after a mileage of 200 thou. km
Thread and flange wear of left wheels of the 1st and the 2nd wheelsets
11

## Slide 19: Universal Mechanism
Predicting wear of railway wheel profiles in program package
"Universal Mechanism": methods and approaches