## Slide 1
Study on the dynamic response of the
heavy haul train running on the
reverse curve railway line
Zhou Shuang
Beijing Jiaotong unversity
PengShan, 2018-10-19

## Slide 2
Extensive attentions of many countries especially those with large size, rich resources, and large quantities of coal and ore are attracted by the heavy haul railway transportation due to its characteristics of large capacity, high efficiency and low transport cost. The success of the haul railway depends on the railway line. The haul railway at home and abroad has been studied deeply, however further studies are needed to meet the rapid development requirements of the heavy haul railway in China.
Background
The safety and stability of the running train is affected significantly by the parameters of the heavy haul railway line, however there is slim chance to avoid the reverse curve railway lines with the limit of the topography and other factors, so to choose the reasonable parameters of the heavy haul railway line is an important factor to ensure the safety and stability of heavy haul train running on the reverse curve railway line, and it is necessary to study on the dynamic response of the heavy haul train running on the reverse curve railway line. The influence of curve radius, length of circular curve, ultra-high, length of intermediate straight line and length of easement curve of the reverse curve railway line on the dynamic response of haul trains was studied in the paper.

## Slide 3
Tian studied the dynamic characteristics of heavy haul trains comprehensively, including the dynamic characteristics of trains influenced by the parameters of the planar line and the ramp.
Cheng studied the running safety and stability of vehicles influenced by the parameters of small radius curve of heavy haul trains by changing the speed of the vehicle and the radius of the curve, and some of the conclusions were obtained.
Chen studied the dynamic characteristics of non-accelerating vehicles and accelerating vehicles when passing the small radius curve through the field test, and it was pointed the passage capacity of the accelerating vehicles was smaller than that of the non-accelerating vehicles when passing curve.
Yi established a theory based on the dynamics of vehicle coupled with line to determine the minimum of the radius of curve of high-speed railway, and the model between the dynamics of vehicle coupled with line and the parameters of the curve under the condition of the ideal orbital geometry to get the allowable parameters of the curve line.
Lu got the maximum of the influence range of lateral force and longitudinal force in a reverse curve line by studying dynamic characters of the structure of the reverse curve line caused by the passing heavy haul trains, and the most unfavorable position was where the curve line changes when the heavy haul trains passing by, and there was adverse impact on running safety where the gauge suddenly increased.
Li studied the dynamic characters of vehicles influenced by the parameters of flat profile of the heavy haul line, and the principle how to select the parameters of the heavy haul line was got.
Stanislav Hodas studied the design parameters of the line, and the corresponding dynamic parameters and the minimum of the horizontal and vertical curve were studied by establishing the 3D model when the train passing by at the speed of 160km/h, 200km/h, 250km/h, 300km/h.
Z.Krzysztof studied the dynamic characters of vehicles influenced by the radius of the curve, ultra-high and the speed of vehicles when the vehicle running on the curve line.
Review

## Slide 4
There are lots of frictional contacts and elastic contacts between various parts of the train due to heavy haul train is a complex multi-body system, so the reasonable simplification of the train model was carried out according to the actual situation.
The C80 model of the truck composed of one body and two bogies is established by using UM software, as shown in the figure. Each bogie is composed of a shaking pillow, two side frames, two wheel pairs and two shock absorbing systems (including friction and contact shock absorbing). It is assumed that the train body, the shaking pillow, side frame and wheel pair are rigid bodies, so each rigid body has 6 DOFs, and one truck has 66 DOFs. Ten train bodies were marshaled together by using the coupling connection in the UM, and the LM wear type tread of the wheels based on the Chinese standard were adopted, and the track structure was simplified into a massless viscoelastic force meta-model, and which was matched with the 75 kg/m standard section rail, and the Kalker nonlinear rolling contact theory was taken as the wheel-rail contact relationship, and the track irregularity was not considered for eliminating the influence of the track irregularity inhomogeneity on the line parameters when the simulation analysis was carried out. The situation of the line was just as shown in the figure.
Dynamics Model of Vehicle Coupled with Line

## Slide 5
Study on the dynamic response of trains under the influence of circular curve radius and train speed
Ultra-high was defined as that when the train running on the circular curve, and slip appeared due to effect of the transverse force and centrifugal force, and to ensure the safety, stability of the train, and to meet the design speed, and ensure the train passed through the circular line economically and comfortably, so the one-way cross-sectional slope which the outer edge was higher than the inside in the cross section to offset the centrifugal force generated from the vehicles running on the circular line. Ultra-high in the curve line is one of the most important factors to be considered in the design of the line. Besides, ultra-high was affected by the speed of train and curve radius, so they were taken together into consideration.
The top surface of two rails should be in a straight line according to the specification. Ultra-high should be set in the curve line, and the ultra-high of the curve line in the new railway lines can be calculate as follows:
Where
h —ultra-high of the outer rail(mm)；
R—radius of the curve(m)；
vmax—maximum of the train speed running on the line of this section(km/h)。
The maximum of the ultra-high should be no more than 150 mm according to the specification
Analysis of the dynamic response of the vehicle

## Slide 6
Study on the dynamic response of trains under the influence of circular curve radius and train speed
The calculated ultra-high referring to the specification and the actual highest one was deemed as the simulated ultra-high. The length of circular curve, easement curve and intermediate straight line are each 100 m, and the radius of circular curve and the speed of the train just were shown in the table below:
Analysis of the dynamic response of the vehicle
The simulation calculation was carried out according to the set working condition, and the maximum of horizontal and vertical acceleration, horizontal and vertical wheel/rail force, derailment coefficient, and the rate of wheel load reduction, and the minimum of vertical wheel/rail force are extracted.
The maximum and minimum of vertical wheel/rail force and derailment coefficient were taken as the example, just as shown in figure.
The maximum derailment coefficient force using the calculated ultra-high
The maximum derailment coefficient force using the actual ultra-high

## Slide 7
Study on the dynamic response of trains under the influence of circular curve radius and train speed
Analysis of the dynamic response of the vehicle
The minimum vertical wheel/rail force using the calculated ultra-high
The minimum vertical wheel/rail force using the actual ultra-high
The maximum vertical wheel/rail force using the calculated ultra-high
The maximum vertical wheel/rail force using the actual ultra-high

## Slide 8
Analysis of the dynamic response of the vehicle
Study on the dynamic response of trains under the influence of the length of circular curve
The calculated ultra-high referring to the specification and the actual highest one was deemed as the simulated ultra-high. The length of circular curve and intermediate straight line were both 100 m, and the radius of circular curve was 6000 m, and the speed of the train was 80 km/h, and the length of the easement curve just were shown in the table below:
The simulation calculation was carried out according to the set working condition, and the maximum of horizontal and vertical acceleration, horizontal and vertical wheel/rail force, derailment coefficient, and the rate of wheel load reduction, and the minimum of vertical wheel/rail force are extracted.
The maximum and minimum of vertical wheel/rail force and derailment coefficient were taken as the example, just as shown in figure.
Maximum of vertical wheel-rail force
Derailment coefficient
Minimum of vertical wheel-rail force

## Slide 9
Study on the dynamic response of trains under the influence of the length of transition curve
The calculated ultra-high referring to the specification and the actual highest one was deemed as the simulated ultra-high. The length of circular curve and intermediate straight line were both 100 m, and the radius of circular curve was 6000 m, and the speed of the train was 80 km/h, and the length of the easement curve just were shown in the table below:
Analysis of the dynamic response of the vehicle
The simulation calculation was carried out according to the set working condition, and the maximum of horizontal and vertical acceleration, horizontal and vertical wheel/rail force, derailment coefficient, and the rate of wheel load reduction, and the minimum of vertical wheel/rail force are extracted.
The maximum and minimum of vertical wheel/rail force and derailment coefficient were taken as the example, just as shown in figure.
Maximum of vertical wheel-rail force
Derailment coefficient
Minimum of vertical wheel-rail force

## Slide 10
Study on the dynamic response of trains under the influence of the length of intermediate straight line
The calculated ultra-high referring to the specification and the actual highest one was deemed as the simulated ultra-high. The length of circular curve and intermediate straight line were both 100 m, and the radius of circular curve was 6000 m, and the speed of the train was 80 km/h, and the length of the easement curve just were shown in the table below:
Analysis of the dynamic response of the vehicle
The simulation calculation was carried out according to the set working condition, and the maximum of horizontal and vertical acceleration, horizontal and vertical wheel/rail force, derailment coefficient, and the rate of wheel load reduction, and the minimum of vertical wheel/rail force are extracted.
The maximum and minimum of vertical wheel/rail force and derailment coefficient were taken as the example, just as shown in figure.
Maximum of vertical wheel-rail force
Derailment coefficient
Minimum of vertical wheel-rail force

## Slide 11
The trends of dynamic response of trains under the influence of circular curve, easement curve and length of intermediate straight line were same with the case of using the calculated ultra-high referring to the specification and the actual one.
The maximum of the dynamic response of train increases with the decrease of curve radius and the increase of the speed of the train, and the minimum of vertical wheel-rail force decreases with the decrease of curve radius and the increase of the speed of the train with the case of using the calculated ultra-high referring to the specification and the actual one.
The maximum of the dynamic response of train decreases with the increase of the length of circular curve, and the minimum of vertical wheel-rail force increases with the increase of the length of circular curve.
The maximum of the dynamic response of train decreases with the increase of the length of transition curve, but the decrease decreases, and then gradually tends to stabilize; the minimum of vertical wheel-rail force increases with the increase of the length of transition r curve, but the increase decreases, and then gradually tends to stabilize.
The maximum of the dynamic response of train decreases with the increase of length of intermediate straight line, but when length of intermediate straight line is less than 20 m, the maximum decreases sharply, and the analysis results show that the intermediate straight line was not allowed in the reverse curve.
The dynamic response of train varied greatly using the actual ultra-high than that of using the calculated ultra-high, and the maximum of the dynamic response of train using the ultra-high was larger that of using the calculated ultra-high, and the minimum of vertical wheel-rail force using the actual ultra-high was smaller that of using the calculated ultra-high
Conclusion

## Slide 12
Exchange and cooperation
with the UM company

## Slide 13
Thanks for your attention！